## Slide 1: Memory Hierarchy

## Slide 2: Memory Hierarchy
Multiple levels of memory with different speeds and sizes
  memory: any medium that can store data (e.g., DRAM, disk …)
registers
CPU Cache
L1/L2/L3
SRAM
(Main memory)
DRAM
(Secondary Storage)
Flash Drive (SSD)
Magnetic disk
(Archival Storage)
Tape drive
faster, smaller
cheaper
0.5~2.5 ns
$500~$1000 per GB
50~70 ns
5-50 µs
5-20 ms
$10~$20 per GB
$0.75~$1.0 per GB
$0.05~$0.10 per GB

## Slide 3: Data in Memory Hierarchy
Block (or line)
  Minimum unit of information
Hit
  When data is present in the upper level
Hit rate (hit ratio)
  Fraction of memory access that is ‘hit’
Miss, miss rate
Miss penalty
  Time to copy a block from the lower level
In this chapter, cache lies between CPU and the main memory
  Cache can exist in many levels

## Slide 4: Cache Memory
Cache memory
  Faster but smaller memory that holds data temporarily to improve the access time of a slower memory
Underlying principle of Cache
  Principle of Locality
    Programs tend to access the same data in a near future
    Temporal locality
      If data is accessed, it is likely that it will be access again soon
    Spatial locality
      If data is accessed, it is likely that near-by data will also be accessed soon
Cache memory is smaller than the lower level memory
  Select only a small set of data to store in the cache

## Slide 5: Cache Access
Assume that:
  CPU requests one word at a time
  Block size is one word
Memory access: X1, …, Xn–1, Xn
Cache placement issue

## Slide 6: Direct-mapped Cache
In direct-mapped cache:
  Cache location is determined as a function of the memory address
  A block (word) can go into only one place in the cache
    fully associative cache
  Cache slot = (word address) mod (# of cache blocks)
# of cache blocks are in power of 2
  Blocks that go into location 001
    00001
    01001
    10001
    11001
000
001
010
011
100
101
110
111
00001
01001
10001
11001
00101
01101
10101
11101

## Slide 7: Direct-mapped Cache
Multiple block maps to one location in the cache
  How do we know which address the block came from?
    Block in 001 comes from 00001, 01001, 10001, 11001
Tags
  High-order bits of the address – 00001, 01001, 10001, 11001
000
001
010
011
100
101
110
111
00001
01001
10001
11001
00101
01101
10101
11101
value
tag
valid
??
??
0
1
0
0
0
1
0
0
010101…110111
010101…110111
000001…110001
000001…110001

## Slide 8: Address Subdivision
Address is divided into tag part and index part
  tag part: 20 bits
  index part: 10 bits
Total number of bits in the cache
  valid bit: 1
  tag bits: 32-(n + m + 2)
  data bits: 2mx32
n: number of index bits
m: 2m is the # of words
4KB cache

## Slide 9: Block Size and Miss Rate
Larger block size
  Miss rate:
  increase/decrease?
  * What about larger cache size?
Miss penalty
  Time to load load a block from MM(Main memory) to Cache
    Set-up time + transfer time
  Reducing the miss penalty (by hiding the transfer time)
    “early-restart”  more effective for instruction than data
    “critical word first”

## Slide 10: Cache Miss Handling in Processor
Separate cache for instruction and data stream
  Instruction and data cache at L1
Cache miss on instruction
  Send PC-4 to memory unit
  Instruct MM (main memory) to perform read
  Wait until data is ready
  Write data to cache entry, fill up the tag and valid fields
  Re-send instruction address to the memory – hit!
(advanced) Improving the cache performance
  Out-of-order execution: non-blocking cache
  Victim cache – small (fully associative) cache holding the replace blocks
Processors | MIPS32 74K Atheros AR9344 | Intel i7-4770 | Apple A10 | ARM Cortex-A57
Instruction cache | 32KB, 32B line, 4-way | 32KB, 64B line, 8-way | 64KB, 64B line, 4-way | 48KB, 64B line, 3-way
Data cache | 32KB, 32B line, 4-way | 32KB, 64B line, 8-way | 64KB, 64B line, 4-way | 48KB, 64B line, 2-way

## Slide 11: Write Handling in Cache
Write-through cache
  Write operation completes after updating the main memory and the cache
  Data consistency maintained
Write-back cache
  Write operation completes after only updating the cache
  Main memory is synced only when a block is replaced from cache
CPU
Cache
Main Memory
X’
X
CPU
Cache
Main Memory
X’
X’
sw instruction
sw instruction

## Slide 12: Cache Performance
CPU time
  Normal execution: includes cache hit time
  Memory stall cycle: cache miss penalty
Assume the read and write miss penalties are the same
  Write-through: complication from write buffer
  Write-back: potential stall from sync when a block is replaced

## Slide 13: Cache Performance
Instruction cache miss rate: 2%
Data cache miss rate: 4%
Ideal case CPI: 2
Question: How much faster is the processor with perfect cache?
  Number of instructions: N
  Instruction miss and data miss are separate
    total penalty cycles = inst miss cycles + data miss cycles
  inst miss cycles = N x 2% x 100 = 2N
  data miss cycles = N x 36% x 4% x 100 = 1.44N
  Total cycles = 2N + 2N + 1.44N = 5.44N
  Total cycles for perfect cache = 2N
  Performance is better by 5.44N/2N = 2.72
Miss penalty: 100 cycles
Load and store: 36% of instructions

## Slide 14: Associative Cache
Direct-mapped cache: a block can be placed in one location
Fully associative cache: a block can be placed anywhere in the cache
Set associative cache: more than one location, but not anywhere (e.g., n-way set associative cache)

## Slide 15: Associative Cache
Direct-mapped cache and fully associative cache are special cases of set associative cache
  direct-mapped: one-way set associative
  fully associative: n-way set associative
Advantage of associative cache
  Decreased miss rate
Disadvantage
  Longer hit time
    All tags within the set must be compared and selected
  Higher H/W cost

## Slide 16: 4-way Set Associative Cache Schematic
longer hit time
higher cost

## Slide 17: Multi-level Cache
Modern processors have more than 1 level of cache
  L1, L2, shared L3 cache on chip
L1: small, fast
L2: larger, slower
  higher associativity, larger block size
  Access time is less critical than L1
L1 cache miss  served by L2 cache
  L2 cache miss  served by L3 cache
Processor
L1 Cache
L2 Cache
L3 Cache
memory address
Main Memory
A
A
A

## Slide 18: Multilevel Cache Performance
Performance with L1 Cache only
  i) Avg CPI = 1 cycle x 1.0 + 400 cycles x 0.02 = 9
  ii) Avg CPI = 1 cycle x 0.98 + (400+1) cycles x 0.02 = 0.98 + 8.02 = 9
Performance with L2 cache
  i) Avg CPI = 1 cycle x 1.0 + 20 cycles x 0.02 + 400 cycles x 0.005 = 3.4
  ii) Avg CPI = 1 cycle x 0.98 + (20+1) cycles x 0.015 + (400+20+1) cycles x 0.005 = 3.4
Performance comparison
Base CPI | 1.0
Clock rate | 4 Ghz
L1 Miss rate | 2%
Main memory access latency | 100 ns
L1 Cache
MM
100 ns
1 cycle
2%
L1 Cache
MM
L2 Cache
1 cycle
2%
5 ns
100 ns
0.5%